### Steps for linking Matlab and coppeliaSim
1. Download the coppeliaSim educational version for the own O.S. from the website:
http://www.coppeliarobotics.com
2. Copy the files that are present inside the coppelia subfolder
~/programming/remoteAPIBinding/matlab
into the own work folder.
3. In the same folder also copy the library present in
~/programming/remoteApiBindings/lib/lib
(you can find a .dll, .dylib or .so file according to the O.S., pay attention to 32/64 bit for	Linux)
4. Open the proper file *.ttt (it is simply the default scene with the chosen robot model where the pre-existent LUA script has been deleted);
5. Start the simulation on coppeliaSim. The program automatically runs as server on the door 19997
6. Launch the file SimpleTest.m on Matlab. The program should read the number of objects present in the V-REP scene and it should end.
### Steps to provide coppeliaSim with target points to joints from Matlab
After executing the previous steps simply launch main_template.m on Matlab. The robot performs sinusoidal trajectories in the joint space.
The code section to modify for the input of the own kinematic control code is specified in the file.